## Slide 1: P5: Prediction of Particle Trajectories using AI
AMS Lab Projects Final Presentation
Autonomous Multisensor Systems Group
Institute for Intelligent Cooperating Systems
Faculty of Computer Science
Otto von Guericke University Magdeburg
17.09.2026
Guru Prasad Vastrala
Hari Charan Hosakote Lokesh
Hrishikesh Vijay Joshi
Jayakrishna Ajithkumar Jayasree

## Slide 2
Motivation
1. Industrial Need
Rotating drums and mixers: cement, pharma, food.
2. Computational Bottleneck
DEM resolves every contact — hours of HPC per run.
3. Real-time Control
A trained surrogate runs the same case in seconds.
DEM reference run — Angle of Repose
This is exactly what the GNN surrogate learns to reproduce with the same settling behaviour, without re-running the solver.

## Slide 3
AI Surrogates: Advantages & Limitations
Advantages:
Replaces the DEM solver at inference. Real-time twins.
Learns contact behaviour from data, no calibration.
Limitations:
Needs expensive high-fidelity DEM runs up front.
Accuracy is limited to the trained domain.
DEM reference run — MoreFlow (granular flow)
Dynamic flow — the harder case for the surrogate.

## Slide 4: Machine Learning as an Alternative to DEM
How ML replaces DEM:
Graph Representation: Particles are nodes, neighbour interactions are edges.
GNN Modelling: Learns physics from trajectory data to predict future positions without runtime solvers.
Why it's a strong alternative:
Performance & Flexibility: Achieves massive speedups over DEM and generalizes to unseen conditions.
Efficiency & Integration: Learns contact parameters implicitly and supports real-time control or digital twins.
Fig 1
Fig 2
DEM (classical solver)
Detect
contacts
Contact-force
law
Integrate
positions
hours
per run
GNN surrogate (GNS)
Particles →
graph
Learned
update
Next
positions
seconds
per rollout

## Slide 5
Literature Review
Sanchez-Gonzalez et al. (2020) Learning to Simulate Complex Physics with Graph Networks(2020)
Main principle: encode the particles into a neighbour graph, process it by message passing, then decode each particle’s acceleration.
Kumar & Vantassel (2023) GNS: A Generalizable Graph Neural Network-based Simulator for Particulate and Fluid Modeling (JOSS, 2023)
Main principle: an open-source PyTorch simulator that learns particle dynamics straight from trajectory data — no contact laws to calibrate.
Fig 3
Fig 4
Encoder
GNN – Message Passing
Decoder
Input state X
Encoder
G⁰
Processor
GN¹
⋯
GNᴹ
Gᴹ
Decoder

## Slide 6
Overall Workflow
6
1. DEM Simulation
LIGGGHTS solver
AOR + MoreFlow
Δt = 10⁻⁴ s
2. Data Preparation
400 CSV → .npz
Honest train/test split
(dynamic phase held out)
3. Graph Construction
particles → nodes
R = 6 mm, ~50 neighbours
pos + 5 velocities
4. GNS Training
encode-process-decode
200,000 steps
NVIDIA H100 (ANTS)
7. Ensemble Kalman Filter (EnKF)
corrects long-rollout drift
stabilises trajectories
correction interval = 20
8. Transfer Study (planned)
AOR ↔ MoreFlow
does the surrogate
generalize?
6. Rollout Evaluation
RMSE · MAE · R²
3,000 & 4,000 particles
vs DEM ground truth, full range
5. Hyperparameter DOE
R ∈ {1.2, 2.5, 6.0} mm
10k vs 200k steps
AOR vs MoreFlow
→
→
→
↓
←
←
←

## Slide 7
Dataset Details
7
Fig 5: Actual frame-400 particle positions,
both datasets: AOR settles into a dome| MoreFlow into a ring.
Fig 6: 25 batches of ~672 particles inject every 10 frames

## Slide 8
Data, Graph Construction & Training Setup
8
Train / evaluation split actually used for the AOR results shown

## Slide 9
Intermediate Results: AOR
Metric | Value
RMSE | 6.90e-04 m
MAE | 4.12e-04 m
R² | 0.9995
Training Time | 8h 30m
Metric | Value
RMSE | 5.42e-04 m
MAE | 3.87e-04 m
R² | 0.9995
Training Time | 9h 30m
3000 Particles
4000 Particles
2000 Particles
Metric | Value
RMSE | 6.86e-04 m
MAE | 4.35e-04 m
R² | 0.9993
Training Time | 4h 42m
Metric | Value
RMSE | 5.58e-04 m
MAE | 3.38e-04 m
R² | 0.9996
Training Time | 2h 26m
1000 Particles

## Slide 10
Results AOR
10
 | Baseline RMSE | EnKF RMSE | R² (base→EnKF) | Improvement
3000p | 5.03e-03 m | 5.40e-04 m | 0.9617 → 0.9996 | 9.3x
4000p | 5.97e-03 m | 4.62e-04 m | 0.9451 → 0.9997 | 12.9x
Fig 7
Fig 8

## Slide 11
Drift Correction – Error Reduction
11
3000-Particles
4000-Particles

## Slide 12
Dynamic GNS + EnKF Rollout
12
3000p — Baseline
3000p — EnKF (interval = 20)
4000p — Baseline
4000p — EnKF (interval = 20)
Click each clip to play. Left: ground truth vs. prediction rendered side by side.

## Slide 13
Intermediate Results: MoreFlow
Metric | Value
RMSE | 4.41e-03 m
MAE | 3.08e-03 m
R² | 0.9902
Training Time | 5h 07m
Metric | Value
RMSE | 4.84e-03 m
MAE | 3.69e-03 m
R² | 0.9881
Training Time | 7h 08m
3000 Particles
4000 Particles
2000 Particles
Metric | Value
RMSE | 4.61e-04 m
MAE | 3.31e-04 m
R² | 0.9997
Training Time | 1h 15m
Metric | Value
RMSE | 3.90e-04 m
MAE | 2.72e-04 m
R² | 0.9999
Training Time | 0h 45m
1000 Particles
Takeaway: error stays below 5×10⁻⁴ m up to 2,000 particles, then rises an order of magnitude at 3,000+.

## Slide 14
Dynamic GNS Rollout Result
3000-Particles
4000-Particles
Baseline GNS rollout(without the Kalman filter) tracks the DEM reference closely frame-by-frame at both particle counts, confirming the surrogate reproduce the granular flow before any correction

## Slide 15
Dynamic GNS + EnKF Rollout Result
3000-Particles
4000-Particles
Left to right in each clip: Reality(DEM)
Plain GNS
GNS+EnKF

## Slide 16
Drift Correction-Error Reduction
3000-Particles
4000-Particles

## Slide 17
Built a GNS surrogate trained on DEM
Baseline rollout tracks the DEM reference
Left uncorrected, drift still accumulates over long rollouts.
The EnKF correction layer brings this back down by roughly an order of magnitude (9.3x at 3k, 12.9x at 4k) over the full-length rollout.
Together, this moves the surrogate closer to the real-time, reliable prediction industrial control loops (rotating drums, mixers) actually need — closing the loop back to the original motivation.
Conclusion

## Slide 18
Future Work-Reinforcement Learning
Our future work, RL would learn how to dynamically adjust the Kalman Filter parameters so that
EnKF can apply the appropriate correction to particle trajectories.
Cross Domain Transfer Study

## Slide 19
EnKF: It see’s an error, so it correct the particle trajectory
EnKF + RL : It learns how strongly EnKF should correct it.
Impact

## Slide 20
Project Timeline & Future Work
Apr ‘26
May '26
Jun '26
Jul '26
Aug '26
Sep '26
Literature Review
Dataset Prep & Graph Construction
GNS Model Training (AOR/MoreFlow)
Hyperparameter Tuning (DOE)
Rollout Evaluation (RMSE, MAE, R²)
Future Work : Cross-Domain Transfer Study and RL + Enkf
Kalman Filter
Completed / In Progress
Planned (Future Work)

## Slide 21
References
Research Papers
Learning to Simulate Complex Physics with Graph Networks Sanchez-Gonzalez, A., et al., International Conference on Machine Learning (ICML), 2020
GNS: A Generalizable Graph Neural Network-based Simulator for Particulate and Fluid Modeling Kumar, K. & Vantassel, J., Journal of Open Source Software, 2023.
Discrete Covariance Adaptation: Xiong, Wei, & Zhang (2021), Asian Journal of Control — Employs Q-learning to adapt EKF noise covariance, stabilizing non-linear tracking tasks.
Adaptive Noise Tuning: Gu, Li, & Tei (2022), IMCEC — Demonstrates reinforcement learning agents choosing dynamic covariance matrices under uncertain sensor and model noise.
Simulation & Dataset
LIGGGHTS – DEM simulation software used to generate the AOR and MoreFlow datasets.
Software & Frameworks
PyTorch
PyTorch Geometric
Graph Network Simulator (GNS)

## Slide 22: P5: Prediction of Particle Trajectories using AI
AMS Lab Projects — Final Presentation
Thank You For Your Attention!
Sai Preetham Sata
Web: ams.ovgu.de
Mail: sai.sata@ovgu.de